## Slide 1
• C PROGRAMMING
InfusiMetrics
An Embedded C Framework for Real-Time IV Fluid Monitoring and Predictive Depletion Alerting
An Arduino C firmware that senses IV fluid level, predicts depletion with on-device regression, understands plain-English commands, raises an escalating nurse call and reads room temperature and distance, extended with a Python analytics dashboard.
PROJECT TEAM
Mahasri Murugesan
CB.SC.U4CSE25637
Mahitha S
CB.SC.U4CSE25638
Sruthica M S
CB.SC.U4CSE25657

## Slide 2: Why Clinical Wards Require Automated Telemetry
THE PROBLEM
Delayed Air Embolism & Reflux Risks
Manual checks mean empty bags are often noticed too late, allowing air or blood backflow into the cannula.
Unnoticed Flow Cessation
Undetected line blockages or pinched tubing cause interrupted medication delivery without immediate staff awareness.
High Nurse Workload
Frequent manual rounds across multiple beds lead to nurse fatigue and human error, and a patient call can go unanswered during peak shifts.
Lack of Predictive Foresight
Standard gravity-fed infusion sets offer zero analytical data or forecasting regarding exact depletion timing.

## Slide 3: Three-Layer Pipeline: C Firmware to Python Dashboard
SYSTEM ARCHITECTURE
LAYER 1
Arduino C Firmware
Senses level, temperature and distance, runs on-device regression, text commands and the nurse-call logic, drives the displays, LEDs, buzzer and servo, and logs events to SD.
LAYER 2
Serial & SD Logging
DATA, EVENT, STATUS, ENV, DIST and NURSE lines stream over Serial (9600 baud); events and samples are also saved as CSV on the SD card.
LAYER 3
Python Analytics & Dashboard
Scikit-Learn forecasting and a Streamlit dashboard with live cards, sensor and nurse-call status, history chart, command buttons and a query box.

## Slide 4: Eight Core Components Wired to the Arduino Mega
HARDWARE & PIN MAP
Fluid Sensor
Potentiometer on A0, read as 0–100%
16x2 I2C LCD
Level, rate and status (A4/A5)
Buzzer & LEDs
Buzzer 8, red LED 9, green LED 10
Patient Bulb
Glows on pin 2 when level is LOW
Servo Clamp
Pin 6; closes the IV line
SD Card Logger
SPI, chip select on pin 4
GPS (NEO-6M)
TX to pin 3, RX to pin 5
Reset Button
Pin 7; silences the buzzer and clears a nurse call

## Slide 5: Five New Components Added to the Mega
ADDED COMPONENTS
Nurse Call Button
Pin 22; a press sends NURSE,1 to the dashboard
DHT22 Sensor
Pin 23; temperature and humidity every 5 s
HC-SR04 Ultrasonic
TRIG on pin 27, ECHO on pin 28; distance in cm
RGB Status LED
Pins 24, 25, 26; green, amber, red or blinking blue
SSD1306 OLED
I2C on pins 20 and 21; address 0x3C
Shared I2C Bus
LCD (0x27) and OLED (0x3C) share SDA and SCL
New Libraries
DHT sensor, Adafruit SSD1306 and Adafruit GFX
New Serial Lines
ENV, DIST and NURSE join DATA and EVENT

## Slide 6: Four Steps Inside loop()
C FIRMWARE LOGIC
1
Sense
Averages 8 analog readings and maps them to 0–100%.
2
Decide
LOW below 20%. The buzzer re-arms only at 25% (hysteresis).
3
Act
LEDs, bulb, buzzer, LCD and OLED update. Still LOW after 60 s: the servo auto-clamps.
4
Log & Alert
Events and samples go to SD as CSV and to Serial, with a readable alert sentence.

## Slide 7: Four Steps From Button Press to Acknowledgement
NURSE CALL & ESCALATION
1
Press
The patient presses the button on pin 22; the signal is debounced for 40 ms.
2
Alert
The RGB LED blinks blue and the buzzer dings. NURSE,1 and a NURSE_CALL event are sent.
3
Escalate
No reply in 30 s: fast red blink, louder buzzer and NURSE,2 on the dashboard.
4
Acknowledge
The reset button or the command ack clears the call and sends NURSE,0.

## Slide 8: Regression and Anomaly Detection, Written in C
ON-DEVICE MACHINE LEARNING
computeDrainRate() (excerpt)
float computeDrainRate() {
if (histCount < 4) return 0;
// sums over hist[0..n-1]:
// sx, sy, sxy, sxx
float slope =
(n*sxy - sx*sy) /
(n*sxx - sx*sx);
return -slope *
(60000.0 / ML_PERIOD_MS);
}
Least-Squares Drain Rate
Slope over the last 12 readings (one every 5 s) gives drain in % per minute.
Time-to-Empty & Early Warning
Level ÷ rate predicts time to empty and to LOW, with a chirp before LOW is hit.
Leak & Blockage Detection
Short-term rate is compared with a learned baseline rate to flag a leak or a blockage.

## Slide 9: Plain-English Control Through the Serial Monitor
NATURAL-LANGUAGE COMMANDS
Intent Recognition
Keyword matching with strstr_P maps phrases like 'how long is left' to the right action.
Entity Extraction
Reads the number after 'bed' or 'room' (e.g., 'status of bed 1') with atoi.
Alert Generation
Builds readable sentences: bed, level, minutes to empty and location.
TRY TYPING
status • how long is left • silence alarm • temperature • distance • ack

## Slide 10: Core Language Features Used in the Firmware
C PROGRAMMING CONCEPTS
Data Types
int, float, bool, uint8_t, unsigned long
Arrays
12-reading sliding window in hist[]
Functions
Modular: readLevel(), mlUpdate(), processCommand()
Pointers & Strings
const char*, strstr_P, atoi, snprintf
Control Flow
if/else, for, while and state flags
Non-blocking Timing
millis() instead of delay(); also times debounce and escalation
Pass by Reference
Print &out writes to SD or Serial
Memory Saving
F() and PROGMEM keep text in flash

## Slide 11: Dashboard & Forecasting Built on the Firmware Data
PYTHON EXTENSION
Log Ingestion
One background thread reads the DATA, EVENT, ENV, DIST and NURSE lines from the Wokwi serial port.
Scikit-Learn Forecast
Linear regression on 5+ readings produces the Next IV Level Estimate.
Streamlit Dashboard
Live cards, sensor and nurse-call status, history chart, command buttons and a query box ('iv low').
The C firmware is the core; the Python layer extends it with visualization.

## Slide 12: Serial Lines Streamed From the Arduino to the Dashboard
DATA FLOW
Serial Line | What the Arduino Sends | Shown on the Dashboard
DATA | DATA,ms,level every 5 s | Level card and history chart
EVENT | EVENT,ms,level,name,rate,lat,lon on LOW, LEAK_SUSPECTED, NURSE_CALL and similar | Recent events and drain rate
STATUS | Level, rate, low, clamped and demo-simulation state every 5 s | Low alert, clamp status, Arduino status
ENV | ENV,temperature,humidity every 5 s | Temperature and humidity cards
DIST | DIST,distance_cm every 5 s | Ultrasonic distance card
NURSE | NURSE,0 idle NURSE,1 calling NURSE,2 unanswered | Nurse alert banner

## Slide 13: How InfusiMetrics Surpasses Traditional Solutions
COMPARATIVE ANALYSIS
Feature Parameter | Traditional Solutions | InfusiMetrics (Proposed)
Monitoring Method | Manual visual check by nurses at intervals | Continuous C-firmware sensing with live LCD and OLED status
Alert Mechanism | Basic local buzzer or patient call button | Buzzer, LEDs, patient bulb, GPS location and servo auto-clamp
Nurse Call | Call button only; nothing follows if nobody answers | Buzzer and RGB cue, escalates after 30 s and shows on the dashboard
Depletion Forecasting | None; purely reactive once bag is empty | On-device regression: time-to-empty, early warning, leak and blockage detection
Room Context | Not measured | DHT22 temperature and humidity, HC-SR04 distance, on the OLED and dashboard
User Interaction | Static charts, paper logs, or fixed LCDs | Plain-English Serial commands plus a Python dashboard with command buttons

## Slide 14: Validated Results from the Python Dashboard
RESULTS
29%
Live Telemetry
Wokwi sensor reading of 29% fluid level displayed live on the dashboard metric cards.
35.5%
ML Next-Level Estimate
Scikit-Learn regression produced the 'Next IV Level Estimate' once 5+ valid readings were buffered.
iv low
NLP Query Result
The query returned 'No low-level alert is currently reported', matching the simulation state.
1 thread
Stability Fix
Setting OPENBLAS_NUM_THREADS=1 resolved the OpenBLAS memory error; the dashboard now runs.

## Slide 15: Expanding InfusiMetrics for Scalable Clinical Deployment
FUTURE SCOPE
IoT Wireless Integration
Replace serial USB communication with Wi-Fi/ESP8266 modules to send alerts and unanswered nurse calls to mobile nursing stations.
Multi-Bed Ward Scaling
Connect many bed monitors (each with its own BED_ID) to one centralized nursing dashboard.
Advanced Time-Series Models
Upgrade linear regression to ARIMA or LSTM networks for long-duration depletion forecasting.
Clinical Safety Expansions
Add optical bubble detectors to help prevent air embolisms.

## Slide 16
Conclusion
Using embedded C for sensing, control, on-device regression, text commands and an escalating nurse call, extended by a Python dashboard, InfusiMetrics demonstrates a scalable approach to improving patient safety and reducing nursing workload.
Thank You!
PROJECT TEAM
Mahasri Murugesan
CB.SC.U4CSE25637
Mahitha S
CB.SC.U4CSE25638
Sruthica M S
CB.SC.U4CSE25657